## Slide 1: The Perfect Brew:
How many yeast cells do we need?
Adapted from:
Consani, A., Doyle, D., Jones, D. L., Sarraj, B., Seitz, H. (2020). The Perfect Brew: An Activity Demonstrating Cell Counting and Hemocytometer Use. QB@CC Spring 2020 Incubator 3, (Version 1.0). QUBES Educational Resources.

## Slide 2: How many yeast cells do we need?
You are a novice home brewer and are very excited to be trying out your very first batch.
You have all the basics ready, but the part of brewing you are still struggling with is the yeast to use.
You have done your research, spoken with some local breweries, and have figured out the strain of yeast to use to give your beer a distinctive flavor.
The only thing you have left to do is to figure out how much yeast to use in your batch.

## Slide 3: How many yeast cells do we need?
From your research you have learned that the perfect amount of yeast is 1.5 million cells/ml
The amount of yeast can be critical, because these single-celled organisms are responsible for converting the sugar in your mixture into alcohol and producing carbon dioxide as a by-product.
  Having too much yeast may make your beer bitter and too carbonated.
  Having too little yeast may make your beer have a low percentage of alcohol and perhaps too sweet. You want to get this just right!

## Slide 4: Part 1: Tools for counting?
To count cells, like yeast, we use a specialized instrument called a hemocytometer.
  A special microscope glass slide with two identical cell counting areas for counting two different samples at a time.
  It comes with a special cover slip for accurate cell counting.
  Once you have a liquid solution of your yeast cells, you can use this special slide on a microscope to see the cells.
  (See more photos like this at https://www.hemocytometer.org/)

## Slide 5: Part 1: Tools for counting?
Before use, the hemocytometer is covered with a special cover slip (thin piece of glass) that spans the two counting chambers.
Using a 20-μl micropipette, the cell volume is usually mixed with an equal volume of cell viability stain such as Trypan blue.
It’s important to count the cells that are alive in your sample as they are the cells that will be able to ferment your sugars and produce alcohol.
https://www.jove.com/v/5048/using-a-hemacytometer-to-count-cells

## Slide 6: Hemocytometer
When you zoom in on the microscope you can see a grid
There are two of these grids on each hemocytometer slide.
The cell counting area of the hemocytometer is composed of 9 large squares
  Marked in red
Each of the 9 is 1x1 mm.

## Slide 7: Hemocytometer
The four corner squares are further divided into 16 identical squares
  Marked in green 0.25 mm each side.

## Slide 8: Hemocytometer
The middle large square is divided into 25 identical squares
  Marked in yellow 0.2 mm each side
Each of these 25 squares are further divided into 16 squares each
  Marked in blue 0.05 mm each side
What is the area of the yellow square shown?
(0.2 mm x 0.2 mm) 0.04 mm2

## Slide 9: Visualizing the volume of liquid

## Slide 10
First let us look at a 1 mm by 1 mm by 1 mm box (shown as the yellow box), and we define that as a microliter.
How many of these boxes are in a cube that is 1 cm by 1 cm by 1 cm?
Hint: 10 mm = 1 cm
So this would be:
1 cm (10 mm) X 1 cm (10 mm) X 1 cm( 10 mm) = 1 cubic cm (1 cc) or 1000 cubic mm
What liquid volume would this box hold?
That would mean that using standard metric notation would give us 1000 mL or 1 mL

## Slide 11: Visualizing the volume of liquid
Look at the diagrams and think about the volume of liquid that is covering the yellow square
How deep is the liquid covering the yellow square and how can we calculate this volume?
(0.2 mm x 0.2 mm x 0.1 mm)=
0.004 mm3, or 0.004 μL OR:
Since 1 cm3 = 1 mL and 1 mm3 = 1 μL, you can convert your dimension to cm first

## Slide 12: Part 2: Counting cells
Healthy sample of cells
  Use a dye called Trypan blue
  Acidic dye that cannot get into healthy viable cells
  Dead cells lack a functioning membrane and this allows the Trypan blue to get in, staining the cells blue.
  To accurately count living cells, use Trypan blue dye on the sample and pay attention to whether or not the cells are stained dark blue
Cells don’t always line up nicely
  In some cases the cells can be on top of the gridlines of the hemocytometer; if we count all the cells on the lines we may overcount our sample
  Need rules about whether we count cells that are laying on the lines
  To avoid exaggeration of cell count within the large squares, cells touching the right and lower sides should be excluded

## Slide 13: Part 2: Counting cells
To avoid exaggeration of cell count within the large squares, cells touching the right and lower sides should be excluded

## Slide 14: Counting cells
Sample | Total Cell Count | Viable cell count | Non-viable cell count | Average Viable Cell Count
1 | ~129-150 | ~100-120 | ~29-31 | ~79.2-100.2
2 | ~110-150 | ~80-110 | ~30-40 | 
3 | ~18-22 | ~87-113 | ~105-133 | 
4 | ~10-12 | ~72-85 | ~82-97 | 
5 | ~14-18 | ~57-73 | ~71-91 | 

## Slide 15: Part 3: Calculating Concentration
After counting cells, we need to calculate our estimate for the cell density of the sample.
Cell density is measured as the number of cells per unit volume
Here’s what we need:
  Volume of the space above the yellow square
  Average number of cells from our 5 counts
  Dilution Factor
In our case, we will use our average number of cells from a small square and the volume (mL) of the small square.
Since we diluted our stock solution we need to apply the dilution factor
  Our sample solution is actually much more concentrated than what we viewed in the hemocytometer.

## Slide 16: What is the volume of a yellow square:
0.000004 mL or 0.004 μL or 4 nL
This can be calculated in a few ways:
We calculated that the entire sample area of the hemocytometer is 0.009 mL
  Made up of 9 large red squares
  Each large square is made up of 25 yellow squares
  So divide this volume by a factor of
  9*25 = 225
  0.009 mL/225 = .000004 mL

## Slide 17: What is the volume of a yellow square:
0.000004 mL or 0.004 μL or 4 nL
Another way:
Yellow square is 0.2 mm per side
  So the volume of the yellow square is
  0.2 mm * 0.2 mm * 0.1 mm = 0.04 mm3 Convert to mL: 0.000004 mL

## Slide 18: Dilution Factors
Next, we need the dilution factor of our sample.
We have taken 10 𝛍L of the original cell sample and mixed with 10 𝛍L of trypan blue solution.
This was done to make the process of counting realistic and allow us to see the cells that are alive versus those that are dead
The dilution factor, D, is the ratio of the diluted solution volume to the original sample volume
It’s given by:
D
10 𝛍L / 20 𝛍L = 0.50

## Slide 19: Dilution Factors
A note on dilution factors:
There are a few ways to represent a diluted solution.
Sample:Diluent For example, if we added 20 mL of diluent to 5 mL of our sample solution, we could write 5:20.
Sample:Total so using our example we could write 5:25, since there would be 5 mL + 20 mL = 25 mL total volume of the diluted solution.
There is no consensus on which format is used, so be aware of what format is being used in each instance.
In the above example, the dilution factor would be

## Slide 20: Cell density
Cell density is measured as the number of cells per unit volume.
In our case, we will use our average number of cells from a small square and the volume (mL) of the small square (Step A).
However, since we diluted our stock solution we need to apply the dilution factor, since our sample solution is actually much more concentrated than what we viewed in the hemocytometer. The calculation is:

## Slide 21
dilution factor (D)
  10 𝛍L/ 20 𝛍L= 0.50
volume of yellow square
  0.000004 mL
average number of cells in a small square
  79.2 - 100.2 cells
measured cell density of our yeast sample
79.2 - 100.2 cells___ = 39,600,000 - 50,100,000 cells/mL
0.5 * (0.000004 mL)

## Slide 22: Cell density of example
How does this compare to the cell density we need (1.5 million cells/ml)?
It is much higher than the recommended density.
How should we adjust this sample to give us the correct concentration?
You should add more diluent to reach the recommended density before adding to your brew mixture.

## Slide 23: What are other reasons to count cells?
Used to get blood cell counts (why called a “hemo” cytometer)
To get accurate plating densities during mammalian cell culture
To get an accurate number of cells when performing various assays
Sperm cell counts are often done using a hemocytometer