## Slide 1: How To Georeference
Presentation by Matt Johnson, Texas Tech University
August 2, 2020

## Slide 2: Why Georeference?
Precise locations for where species are
Identify areas for conservation
Predict distributions
Model how distributions will change
Fook 2009, Semantic Scholar 54655079

## Slide 3: Why Georeference?
GPS Coordinates Unavailable Before 2000
Observation records still hold information!
Need to convert it to GPS coordinates: georeference
Source: Texas Tech University E.L. Reed Herbarium
Record TTC021709

## Slide 4: GeoLocate
https://www.geo-locate.org/web/default.html
Converts text to possible GPS coordinates

## Slide 5: GeoLocate
https://www.geo-locate.org/web/default.html
Converts text to possible GPS coordinates

## Slide 6: Georeference
Key Data Points
Latitude
Longitude
Uncertainty
Do not record data point when Uncertainty is over 10,000 m

## Slide 7: Using Google Maps
Sometimes, GeoLocate datapoint not precise enough
Use Google Maps to find addresses and intersections

## Slide 8: Edit Uncertainty
Place a point with the Place Marker
Use the Measure tool to identify the precise location
Click on the point to Edit Uncertainty- you may need to zoom out

## Slide 9: Historical Maps
Locality string from 1966 Texas specimen:
“roadside on st.hwy. 26; 3.5 mi. n. of henderson”
No Highway 26 in Henderson, TX
State Highway TX-26 is in Dallas,
not Henderson, TX

## Slide 10: Historical Maps
Locality string from 1966 Texas specimen:
“roadside on st.hwy. 26; 3.5 mi. n. of henderson”
Click this + for more maps
Check box for Historical Maps
Click on the map to load historical map data
Choose a map relevant for observation
Use slider to control opacity
Look, it’s TX-26 on a map from 1956!

## Slide 11: Measuring Distances
Locality string from 1966 Texas specimen:
“roadside on st.hwy. 26; 3.5 mi. n. of henderson”
Use the Measure tool
Trace the Road 3.5 mi N of Henderson
Switch to “Place Marker” to choose a point
Don’t forget to edit uncertainty!

## Slide 12: Summary
Take your time and use all of the available resources
Record the latitude, longitude, and uncertainty
Avoid being too precise
Have fun with the detective work!