## Slide 1: Groundwater Flow Modeling with Excel
Michael A. Karls
Ball State University

## Slide 2: Abstract
We illustrate a means to study differential equations that model groundwater flow with Excel, in a fashion similar to using commands such as Mathematica’s Manipulate to vary parameters in a model.

## Slide 3: Outline
Groundwater Flow Project
Problem Statement
Mathematical Model
Sand Tank Overview
Data Collection
Initial Results
Revised Problem
Revised Model Results
An Alternative to Using Mathematica
Excel Solver Add-In
Form Controls
Excel Model
Comparison of Mathematica and Excel Models
Conclusion

## Slide 4: Groundwater Flow Project
In Fall 2012, I worked with undergraduate Jeremy Christman on investigating one-dimensional groundwater flow.
This work was supported by a 2012 – 13 STATE Space Grant Consortium grant, a joint award with University 2.
University 1’s role was to study analytical groundwater flow models.

## Slide 5: Problem Statement
Find a time-dependent model for one-dimensional groundwater flow on an interval between two fixed water head levels.
The model should be able to predict water well head levels as a function of position x and time t.
Find a way to measure or collect actual well head levels.
Compare the model to data found.

## Slide 6: Mathematical Model
A model for one-dimensional groundwater flow is the one-dimensional heat equation with appropriate boundary conditions, initial head levels, and hydraulic diffusivity k:
To solve IVBVP (1) – (4), one uses Separation of Variables and Fourier series methods, to find:

## Slide 7: Sand Tank Overview
One way to illustrate groundwater flow is via a Groundwater Flow Model, or “sand tank”, such as the one pictured, from Iowa State University.
A Groundwater Flow Model “is an educational device constructed of sturdy layered sand lenses to represent a sliced section of earth.”
“Through the use of water tinted with food coloring or grape Kool-Aid, it is possible to observe a wide range of groundwater movements”.
Groundwater Flow Model Courtesy of Iowa State University
Chapter of the Soil & Water Conservation Society.

## Slide 8: Data Collection
For data collection, we used a sand tank provided by Ball State’s Department of Geological Sciences.
Green food coloring was added to the water flowing through the model to help see it in the wells.
Using Author 2’s cell phone to film the water levels in wells, we were able to extract well head level data from the video via the free physics demonstration software package Tracker.

## Slide 9: Model Measurements
In addition to well head levels being measured by Tracker, we took physical measurements of the sand tank itself.
A copy of some of our recorded measurements is shown in the figure.

## Slide 10: Initial Results
Model implementation and comparison to measured data were done in Mathematica.
Boundary head levels are measured to be approximately H0 = 0.56 in and H1 = 9.69 in
Head levels are given in inches, over a time interval of about seven seconds.
Model (curves) vs. Data (points) is shown in the figure.
Using Mathematica’s FindMinimum, we find a RMSE of about 0.78 in with k = 8.85 in2/sec.

## Slide 11: Revised Problem
Since the model and data do not agree closely when we use the measured end head levels, let’s try a new approach!
Perhaps the end head level measurements aren’t as accurate as we have assumed.
Let’s assume that the end head levels are unknown and find a solution to the original problem with this added assumption.
Here are two ways to approach this revised problem:
  Replace our steady-state with a linear function that is fit to measured data for large time values.
  Treat the unknown head levels at each boundary as parameters, H0 and H1.

## Slide 12: Revised Model Results with First Assumption
  With our new steady state function, we get a better fit to the data!
For this new model, the RMSE is about 0.14 in, with k = 20.68 in2/sec.
  Note that with this new steady state, predicted values of H0 and H1 are: H0 = 1.81 in and H1 = 6.48 in.

## Slide 13: Revised Model Results with Second Assumption
Treating the boundary head levels H0 and H1 as parameters, we get even better results!
With k = 17.37 in2/sec, H0 = 1.85 in, and H1 = 6.89 in, we find that the RMSE is 0.11 in.

## Slide 14: An Alternative To Using Mathematica
Is there a way to implement these models in a different (cheaper) software package, such as Excel?
The quick answer is YES!
To do so, we will first look Excel’s Solver Add-In and Form Controls.
These can be used to “replace” Mathematica’s FindMinimum and Manipulate commands with analogous operations or commands in Excel.

## Slide 15: Excel’s Solver Add-In
One of the tools in Excel that can be used for optimization problems is the Solver.
To start the Solver, on the Data tab, in the Analysis group, click Solver.
If the Solver command or the Analysis group is not available, you need to load the Solver Add-in program.

## Slide 16: How to Load the Solver Add-In (PC)
Click the File tab, click Options, and then click the Add-Ins category.
In the Manage box, click Excel Add-ins, and then click Go.
In the Add-ins available box, select the Solver Add-in check box, and then click OK.

## Slide 17: How to Load the Solver Add-In (Mac)
On the Tools menu, select Add-Ins.
In the Add-Ins available box, select the Solver Add-In check box, and then click OK.
If Solver Add-in is not listed in the Add-Ins available box, click Browse to locate the add-in.
If you get prompted that the Solver add-in is not currently installed on your computer, click Yes to install it.

## Slide 18: The Solver Parameters Dialog Box
Set Objective - Specifies the objective cell that you want to set to a certain value or that you want to maximize or minimize.
  This cell must contain a formula.
To - Specifies whether you want the objective cell to be maximized, minimized, or set to a specific value.
  If you want a specific value, type it in the box.

## Slide 19: The Solver Parameters Dialog Box (cont.)
By Changing Variable Cells - Specifies the cells that can be adjusted until the constraints in the problem are satisfied and the cell in the Set Objective box reaches its target.
  The adjustable cells must be related directly or indirectly to the objective cell.

## Slide 20: The Solver Parameters Dialog Box (cont.)
Subject to the Constraints - Lists the current restrictions on the problem.
Add - Displays the Add Constraint dialog box.
Change - Displays the Change Constraint dialog box.
Delete - Removes the selected constraint.
Reset All - Clears the current problem settings, and resets all settings to their original values.
Load/Save – Used to load or save Solver scenarios.
Options - Displays the Solver Options dialog box.

## Slide 21: The Solver Parameters Dialog Box (cont.)
Solve - Starts the solution process for the defined problem.
Close - Closes the dialog box without solving the problem.
  Retains any changes you made by using the Options, Add, Change, or Delete buttons.

## Slide 22: The Solver Options Dialog Box
The Solver Options dialog box allows one to control advanced features of the solution process and define parameters for both linear and nonlinear problems.
Each option has a default setting that is appropriate for most problems.
It is best to leave the default settings in place!

## Slide 23: Solver Solution Methods
The Solver has three built-in solution methods.
  GRG Nonlinear (generalized reduced gradient algorithm)
  Simplex LP
  Evolutionary
For most problems one may encounter, choose the default GRG Nonlinear method.
For linear problems, choose Simplex LP.
The Evolutionary method is beyond the scope of the problems I have encountered.

## Slide 24: Example 1
Find a function of the form Y = A*e^(k*t), that minimizes the sum of the squares for error, i.e. minimizes the function 𝚺(yi-Yi)2 for i = 1,2, … n.
t | y
0 | 32800
5 | 55800
10 | 73600
15 | 138000
20 | 202000
25 | 257000
30 | 301000
35 | 584000

## Slide 25: Example 1 (cont.)
Put the given table of data into Excel and add a column labeled Y = A*e^(k*t).
In cell C10 (red cell), use the function SUMXMY2 to compute the sum of the squares of the differences between elements in the y – column and the Y – column.

## Slide 26: Example 1 (cont.)
Choose cell C10 as the Objective Cell, the (blue) cells containing A and k (F2 and F3) as the Changing Cells, and Minimum in the Solver!
Excel finds* that the optimum choices are
  A = 35867.6387 and
  k = 0.07805832

## Slide 27: Example 1 (cont.)

## Slide 28: Form Controls
Form controls consist of items seen in windows programs and dialog boxes such as buttons, scroll bars, spin buttons, list boxes, check boxes, radio buttons, etc.
In order to be able to add form control items, the “developer tab” MUST be added.
To add the Developer Tab:
  PC: File, Options, Customize Ribbon, Check “Developer”
  Mac: Excel, Preferences, Ribbon (or View), Check “Developer”

## Slide 29: Example 2
Repeat the first example.
Let A = 32,800 and vary k to get the “best graphical fit”.
Then find a choice for k that minimizes the sum of the squares for error.
t | y
0 | 32800
5 | 55800
10 | 73600
15 | 138000
20 | 202000
25 | 257000
30 | 301000
35 | 584000

## Slide 30: Example 2 (cont.)
Put the given table of data into Excel and add a column labeled Y = A*e^(k*t).
Choose A = 32,800 (yellow cell) and for parameter k (blue cell), create a spin button form control.

## Slide 31: Example 2 (cont.)
Step 1: Create a “Spin Button”, via
  Developer,
  Insert (Icon),
  Form Controls,
  Spin Button,
  then Drag a Rectangle

## Slide 32: Example 2 (cont.)
Step 2: Set the properties for the “Spin Button”, and link the output of “Spin Button” to a cell reference.
  Right-Click, Format Control, Control
  Minimum Value: 1 ; Maximum Value: 10; Incremental Value: 1 ; Cell Link: I3
  Choose “OK”
  Test the bi-directional link between the “Spin Button” and cell I3.
  Notice how manually changing cell I3 also updates the “Spin Button”.

## Slide 33: Example 2 (cont.)
Step 3: To vary parameter k between 0.01 and 1, put the formula
  =I3/100
  in cell F5.

## Slide 34: Example 2 (cont.)

## Slide 35: Excel Model

## Slide 36: Excel Model

## Slide 37: Initial Model
Mathematica
Excel

## Slide 38: Revision 1
Mathematica
Excel

## Slide 39: Revision 2
Mathematica
Excel

## Slide 40: Conclusion
Excel’s Solver and Form Controls provide a “cost-effective” means to study differential equation models.
The Solver “replaces” Mathematica’s FindMinimum for minimizing error.
Form Controls “replace” Mathematica’s Manipulate for varying parameters in a model.

## Slide 41: Thank You!