## Slide 1: Logjams and Stream Habitats
Dr. Adriana E. Martinez, Southern Illinois University Edwardsville
adrmart@siue.edu

## Slide 2: Dr. Adriana E. Martinez
Associate Professor
Southern Illinois University Edwardsville
Fluvial Geomorphologist

## Slide 3: Riparian zone: Source of Wood
Riparian zone: channel (including side channels, off-channel pools, etc.), plus terrestrial area on either side of river channel
  Wide enough to include all of terrestrial area where direct interaction between terrestrial and aquatic ecosystems occurs
Terrestrial-aquatic interactions: transfer of material from terrestrial to aquatic or vice versa.
  Terrestrial vegetation that falls into stream, sediment inputs to stream from adjacent geomorphic surfaces;
  Surface water exchanges, particularly overbank floods
  Subsurface water exchanges
Importance of transfer of material: food supply for aquatic ecosystem

## Slide 4
Geomorphic floodplain
Q-20yr floodplain
Riparian zone
Riparian zone

## Slide 5: Riparian buffer zones
RBZ is a policy, not a natural entity; defined in regulations
RBZ may be narrower than the floodplain in wide valleys, wider than the floodplain in narrow V-shaped valleys
Typical RBZ width:
  Illinois USACE
    Fully functional: deep-rooted native veg >50 ft wide on both sides
    Moderately functional: deep rooted veg 25-50 ft wide
    Functionally impaired: 0-25 ft
  U.S. Forest Service: Distance from the streambank equal to the height of a “site potential tree”

## Slide 6: Outline
Wood in Streams

## Slide 7: Arrangement of LW in small stream
Watershed 2, Andrews Experimental Forest, channel 2-10 m wide
LW length >> channel width
Random orientation of wood, little or no transport

## Slide 8: Arrangement of LW in medium stream
Mack Creek, Andrews Experimental Forest, 3rd order, channel 10-20 m wide
LW length ≈ channel width
Many pieces oriented downstream, indicating transport

## Slide 9: Arrangement of LW in large stream
McKenzie River at Rainbow, 6th order, channel 40-50 m wide
LW length << channel width
All wood looks transported, no channel-spanning accumulations

## Slide 10: Association of LWD accumulations with anabranching channels
Abbe and Montgomery 2003
Queets River, WA

## Slide 11
Bar apex LWD accumulation, Gate Creek, McKenzie R., after 1996 flood

## Slide 12
Bar apex LWD, McKenzie River, Oregon
Flow

## Slide 13
Dispersed bar apex and top LWD Naches River, Washington, Columbia Basin
Flow

## Slide 14
Chiwawa River, Washington Cascades

## Slide 15: Wood And Channel Morphology

## Slide 16: River Channel Features

## Slide 17: Riffles and Pools

## Slide 18: Island formation by LW
Initial piece of LW, will become the key piece
Increased shear stress
Decreased shear stress
Resulting pattern of scour and deposition
Key piece has caught additional pieces of LW
Abbe and Montgomery 1996, Regulated Rivers 12: 201-221

## Slide 19: Continued development of LW accumulation and bed form
Island begins to emerge
Eventual integration into floodplain
Abbe and Montgomery 1996

## Slide 20: Vegetation succession on wood bar
Fetherston et al 1995, Geomorphology 13: 133-144.

## Slide 21: Silver Creek, Illinois
Control Reach
Logjam Reach

## Slide 22: Large Wood and Stream Restoration

## Slide 23: Wood accumulation on outside of meander bend: natural LWD revetment
Queets River, WA; Abbe and Montgomery 2003
Larger streams, 3rd order and greater
LWD accumulations form on tighter bends but not on more open bends.
LWD accumulation actually protects bank from erosion.
  Natural revetment

## Slide 24: Constructed LWD Revetment
Queets River, WA; Abbe and Montgomery 2003

## Slide 26: Main Takeaways
Riparian zones are a major contributor to logs in streams
Logjams occur naturally and are important
Logjams influence channel morphology
Logjams have been used for stream restoration to create heterogeneous habitat

## Slide 28: Ecological definitions of riparian zone
RZ is the larger of the following:
  Zone extending horizontally on either side of the channel equal in width to the height of dominant tree species (at maturity)
  Zone extending to outer limit of regular flooding (10 yr flood or larger?)
  The lateral extent of hyporheic exchange
Riparian buffer zone: a protected zone defined by a specific width from the channel, for management purposes (i.e. forestry rules, land development permits, etc.)