## Slide 1
Addressing Complex, Emergent Risks in 21st Century
Natural-Human Systems
Jordan Kern, PhD
Research Assistant Professor
Institute for the Environment
Associate Director
Center on Financial Risk in Environmental Systems
Notes: So, a couple months ago I was invited to give a talk at another university, and the topic was supposed to be global environmental change.

## Slide 2
GLOBAL ENVIRONMENTAL CHANGE
A phrase subject to such a broad range of possible interpretations, it begins to mean nothing.
Source: Steffen et al., 2015
Humans are Pushing “Planetary Boundaries”
High risk
Increasing risk
Safe
Not quantified
My research
Notes: Which, is a phrase that can be defined really broadly. So it forced me to think about what exactly this term means to me, and also how my own work seeks to address it. And after a couple days of poking around the literature I kind of latched on to the planetary boundaries concept, which tracks anthropogenic changes in a variety of areas, and also measures those changes against certain thresholds and tipping points beyond which irreversible change is likely to occur. My research involves the areas highlighted in blue, and I’ll touch on each one today. But I think the primary lens through which to view my work is really climate change, and specifically the human response to climate change, which is an issue I take on in two different respects.

## Slide 3
Stationarity is Dead*
* Milly et al., 2008
Source: NOAA, 2017
Increasing Exposure to Extreme Weather Events
2100
2018
Growing Value-at-Risk
Mar-a-Lago, FL
Source: Climate Central
Notes: First, a big part of what I do relates to the exposure of human systems to extreme events in natural systems, and this exposure is increasing, both due to climate non-stationarity, and also due to myopia. Humans are just beginning to incorporate the risks of climate change into long term decisions we make.

## Slide 4
UNC Center on Financial Risk in Environmental Systems
Notes: As part of my research in this area, I’m the associate director of a center at UNC on financial risk in environmental systems, which manages a portfolio of projects broadly distributed across the U.S. that quantify the risks from extreme weather in multiple sectors and develop novel strategies for managing those risks.

## Slide 5
Cascading impacts from the “energy transition” ( renewables, storage, electric vehicles, biofuels)
Freshwater
Estuary
Marine
Anadromous Life Cycle
Global CO2
Emissions
Wind
Hydro
Solar
Geothermal
Biomass
Source: US EIA, 2014
Notes: The second perspective that I bring on humans’ response to climate change has to do with the potential for cascading impacts from the energy transition. A lot of my work focuses on how our efforts to rapidly reduce carbon emissions by switching to renewable technologies will first alter energy market dynamics, and how those altered price dynamics will impact the way we use infrastructure and natural resources, and how this ultimately may impact sensitive ecosystems.

## Slide 6
Humans’ response to climate change: exploring the feasibility of “win-wins”
Emissions reduction
& human adaptation
Micro
-algae
Notes: In studying humans’ response to climate change in terms of both human adaptation and emissions reduction, I’m particularly interested in identifying potential “win-win” scenarios, by which we simultaneously make headway in addressing climate change, while also reducing pressure on other planetary boundaries. An example I’ve worked on in the past is the potential use of algal biofuel production as a mechanism for cost-effectively removing N and P from wastewater effluent in impaired watersheds

## Slide 7
Humans’ response to climate change: tradeoffs and unintended consequences
Emissions reduction
& human adaptation
Solar
Wind
Source: Oakenleaf et al, 2015
Notes: I also deal a lot with how to manage tradeoffs and unintended consequences that result from humans’ response to climate change. In this case, while we make progress on reducing the impacts of climate change, we inadvertently make things worse in other categories. An example of that would be the potential for an increased dependency on low power density resources like wind and solar to pose global habitat conversion risks.

## Slide 8
Engineering
Environmental
Science
Computational modeling, Statistics, & Operations Research
Multi-disciplinary Study of “Systems of Systems”
Finance &
Economics
A phrase subject to such a broad range of possible interpretations, it begins to mean nothing.
Notes: These are highly complex problems that are really difficult to confine within traditional academic depts, because it takes diverse set of skills and expertise to address them. I specialize in what I would call multi-disciplinary study of systems of systems. Now, this is a phrase that, like global environmental change, is pretty broad. So let me take one more stab at definition --this time regarding myself. I am technically an engineer, with a strong background in environmental science and hydrology, who also knows a lot of finance and economics. My main research tools are computational modeling, statistics, and operations research.

## Slide 9
Across value domains, sectors, and stakeholder groups
Multi-disciplinary Study of “Systems of Systems”
Human
Infrastructure
Market dynamics
Natural
Extreme events
Ecosystem health
Uncertainty (policy, technology, weather/climate)
Vulnerabilities Thresholds Tradeoffs
Notes: And I use those to build models of coupled natural-human systems, in order to explore their dynamic interactions under different sources of uncertainty, with the main goal of being able to identify and manage vulnerabilities, thresholds and tradeoffs across objectives.

## Slide 10
Methodological Deep(ish) Dive
Notes: So with that, I’d like to get into some details about my methodological approach. I’m not going to take you on a full bore exploration of all the methods I use, so please stop me if you have any questions, or we can discuss in depth at the end.

## Slide 11
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage
Coupled Water-Energy Systems
Notes: A major part of my research over the last several years has involved the study of coupled water-energy systems, with a primary emphasis on how the electric power sector interacts with freshwater systems.

## Slide 12
Spatially distributed capacity (supply)
100
MW
1000
MW
Coal
Natural Gas
Hydro
Wind
Solar
Nuclear
Notes: To model power systems I start with a spatial representation of generation capacity in the US, and then couple that with

## Slide 13
Spatially distributed load (demand)
Notes: a spatial representation of dynamic load (or demand)

## Slide 14
Kirchoff’s Current & Voltage Laws (DC approx.)
Load (Hub aggregate)
MWh
Peak
0
J F M A M J J A S O N D
Chart: 
Notes: To form an aggregated network representation of the grid. The flow of power is constrained in a way that mostly mimics the laws of physics, and then each one of the nodes is associated with its own respective time series of electricity demand, as well as a specific portfolio of generation resources with which to meet that demand.

## Slide 15
Chart: Hours
0 24 48 72 96 120 144 168
Hourly schedule ( production, costs, emissions, etc.)
Hydro
Demand
Wholesale Price
Wholesale Price
Wholesale Price
Notes: I use simulation-based optimization to identify least cost generating schedule for meeting electricity demand, along with associated metrics of interest, including wholesale prices. For a generation portfolio that looks like this, we can equivalently view it through a micro-economic lens as a system supply or marginal cost curve, and this allows us to estimate wholesale prices and show how they increase if demand goes up, decreases if demand goes down.

## Slide 16
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage
Coupled Water-Energy Systems
Notes: One of the things that can create idiosyncrasies among power systems are their different dependencies on water resources for hydropower production and cooling water at thermal power plants. So to get a complete picture of power system operations, it’s often necessary to integrate consideration of water resource systems.

## Slide 17
Hydrological Modeling
Streamflow
Time
Dam C
Dam B
Streamflow gage
Dam A
Numerical Weather Prediction
Pavelsky et al. (2012)
Liang, X. et al. (1994)
Runoff
Baseflows
K
NLCD
DEM
Land-Atmosphere-
Bio. Interactions
Notes: And that means watershed scale hydrological modeling. There are a couple different options for how to approach this. The translational approach is use numerical weather prediction of temperatures and precipitation to drive hydrological processes on a watershed scale, which yield estimates of distributed streamflows throughout a river and stream network. This approach can be really useful, particularly if you’re interested in how changes in these underlying processes might alter water availability in the future, and I’ve collaborated a lot with folks that do more detailed hydrological modeling.

## Slide 18
Stochastic Hydrology
Dam C
Dam B
Streamflow gage
Dam A
Covariance Structures
Historical or Predicted Future Flows
Gage 1
Gage 2
Gage 3
Gage 4
x
Statistical Moments
MUST REPLICATE:
1
3
2
Autocorrelation
Time
Notes: But at the heart of much of my research is an interest in risk, or assessing system performance probabilistically. As a result, I mostly use the outputs of detailed hydrological modeling to inform my own stochastic representation of streamflow dynamics. I identify historical or future predicted streamflow records at each gage site of interest, and then I create massive synthetic records, not predictions, but very large representative samples. The main objective is to create a synthetic record that replicates statistical characteristics of the historical or predicted future record.

## Slide 19
Runoff
Discharge
Evap
Discharge
Dam Operations
Res
1
Res
2
Food & Urban
Watershed Hydrology
Hydro
MASS BALANCE
Thermal
SUBJECT TO: flood control, environmental flows (minimum flows, ramping)
Water
Demand
Notes: Streamflows are then used as the primary driver of mass-balance operational models for reservoir systems that account for water demands from thermal power plants, irrigated agriculture and urban consumption. The goal of these operational models is really to determine how much water is available for release via hydropower production, and often that volume is highly constrained by storage requirements for flood control and environmental restrictions that ensure minimum flows and/or restrict the ability of the dam to ramp power production and discharge up and down very quickly.

## Slide 20
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage
Coupled Water-Energy Systems
Notes: Then once the structure of the natural-human systems modeling is in place I subject it to uncertainty in key exogenous drivers in order to understand its behavior under stress.

## Slide 21
Weather &
Climate
Technology &
Markets
Population
Growth
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage

## Slide 22
Uncertainty in Exogenous Drivers
Covariance Structures
x
Statistical Moments
Autocorrelation
Time
SHORT TERM and “WELL DEFINED”
Seasonality
Diurnal Effects
Residual Process
Jan June Dec
Stochastic modeling: temperatures, wind speeds, solar insolation, commodity prices, etc.
Monte Carlo
0 24
Notes: There are two ways I think about representing uncertainty in these exogenous drivers. In cases where the uncertainty of a process is well defined (for example temperatures, wind speeds, and commodity prices), I use stochastic modeling to essentially pull out all the mathematical structure of how these variables change dynamically over time, and I use that structure along with Monte Carlo simulation to create synthetic records that we might expect to see in the near future.

## Slide 23
Top-down “States of the world”
  Deterministic climate change
  Land use-land cover regimes
  Renewable energy mandates
  Water quality regulations (TMDLs, thermal pollution)
Bottom-up
  Sensitivity analysis to identify areas of vulnerability
Present
Multiple
Futures
Uncertainty in Exogenous Drivers
LONGER TERM and “DEEPLY UNCERTAIN”
Notes: For situations in which uncertainty is much longer term and less well defined, there are two options. A top down approach, which explores pre-defined potential future ‘states-of-the-world (e.g., using specific climate change projections), and bottom-up modeling, which is more akin to a targeted sensitivity analysis that tries to identify specific thresholds of system vulnerability.

## Slide 24
Weather &
Climate
Technology &
Markets
Population
Growth
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage
Notes: Pushing uncertainty through these coupled natural-humans systems then gives me an ability to evaluate performance in terms of a range of different metrics.

## Slide 25
Weather &
Climate
Technology &
Markets
Population
Growth
Demand
Thermal & Hydro
Food & Urban
Watershed Hydrology
Renewables & Storage
Environmental
Quality
Financial
Risk
Cost &
Reliability

## Slide 26
Environmental Quality and Ecosystem Health
Life Cycle Assessment (power systems, biofuels)
  Emissions
    Greenhouse gases (CO2 equivalent)
    NOx, SO2
    N, P loading
  Resource consumption (e.g., land, water, fertilizer)
Natural flow regime
  A “master ecological variable”* in river ecosystems
  Timing, magnitude, frequency, duration, rate-of-change of streamflows
* Poff et al., 1997
Notes: These I divide conceptually into two different groups, those that address societal risk and those that address risks for individual stakeholders. On the societal level, I focus on environmental quality through life cycle assessment, which is used to estimate the static environmental impacts of different human activities. I also spend a lot of time studying how humans alter what we call natural flow regime. Natural flow regime is the concept that river ecosystems co-evolved alongside watershed processes, to the point that they are interdependent, and river ecosystems rely on the natural dynamism of rivers and streams to sustain themselves.

## Slide 27
Natural Flow Regime
Source: OSU, 2017
Geomorphology (sediment transport, habitat creation)
Floodplain connectivity (nutrient transfer, breeding and feeding ground)
Physiological cues (spring high flows upstream migration)
Invasive species protection (prolonged low flows)
Impacts of Dams
Source: Poff and Zimmerman, 2010
75
50
25
0
Fish
Macro.
Veg.
Aquatic PP.
Birds
Amph.
Altered flow regime & biological endpoints
Number of Papers
Notes: For example, streamflow dynamics are import for sediment transport and habitat creation, floodplain connectivity, initiating and supporting certain life cycle processes, and keeping out invasive species. Dams in particular can have a range of damaging effects on river ecosystems, mostly by eliminating hydrological extremes like low and high flow events. Connecting specific changes in flow regime to biological endpoints can be challenging, but a lot of literature exists on this, with most focused on impacts to fish, macroinvertebrates and riparian vegetation.

## Slide 28
Indicators of hydrologic alteration (IHAs)
Monthly means
Multi-day min/max flow (1,3,7,30,90-day)
Low (<10%) and high (>90%) pulse number an duration
Number and rate of rises/falls
Environmental flow components (EFCs)
More firmly tied to ecological function
Extreme low flows, low flows, high flow pulses, small floods
Sources: Mathews and Richter, 2007
Quantifying dams’ impacts on natural flow regime
Fracking
Wind
Dams
Notes: These studies often try to connect those ecological impacts to quantifiable changes in natural flow regime, measured by a range of environmental flow statistics developed over several years by the Natural Conservancy and others. I use these statistics to perform experiments where I translate technological changes to altered electricity price dynamics, to changes in the operational behavior of dams, and finally to proxies for ecosystem impacts.

## Slide 29
Droughts, floods, heat waves, cold snaps
Losing too much money at the wrong time
Quantifiable probability of recurrence
Environmental Financial Risk
Notes: For individual stakeholders, I focus a lot on evaluating what I call environmental financial risk. In short, this describes situations where a government or business loses a lot of money directly due to exposure to an extreme weather or climate event.

## Slide 30
Financial instruments that make a payment to the policyholder if a triggering event occurs (e.g. extreme weather)
Range of types, applications:
  Catastrophe bonds (hurricanes)
  Temperature derivatives (heat waves, cold snaps)
  Insurance
    Wind speeds, solar insolation (renewable energy)
    Precipitation (crop failure)
    Streamflow (hydropower)
    Ecosystem (natural defense) damage (new!)
    Disease cases (pandemics)
Parametric (index-based) financial hedging
Premium
Policy-
holder
Insurer
Triggered
Payouts
Mesoamerican Reef and Cancún
Notes: I’m also interested in the design of parametric (or index based) financial hedging agreements that can be used to protect against extreme weather and climate events. These can have a variety of forms and applications, include catastrophe bonds, which protect against really big natural hazards like hurricanes, and insurance, which can be customized to cover a variety of undesired environmental outcomes. An exciting recent development is the Nature Conservancy’s development of insurance that can help cities and states fund post-event ecosystem restoration, with the most prominent example being the purchase of insurance by a Mexican state to fund coral reef recovery after hurricanes, which is win-win because coral reefs play an important role in mitigating wave height.

## Slide 31
Notes: So I think that gives you a broad sense of the tools that I use to model different natural-human systems.

## Slide 32
A Sample of Previous Research
Notes: What I’d like to do now is demonstrate how this wide ranging methodology allows me to gain innovative insights into these complex systems.

## Slide 33
Exploring “win-wins”, tradeoffs and unintended consequences
Emissions reduction
& human adaptation
Notes: Almost all of these can be viewed this conceptual framework I presented earlier, of exploring the potential for both win-wins, but also tradeoffs and unintended consequences in the human response to climate change.

## Slide 34
WILL WIND POWER INTEGRATION EXACERBATE DAMS’ IMPACTS on RIVER ECOSYSTEMS?
Kern, J.D., Patino-Echeverri, D., Characklis, G.W. (2014). “The Impacts of Wind Power Integration on Sub-Daily Variation in River Flows Downstream of Hydroelectric Dams.” Environmental Science and Technology. Vol. 48, No. 16, pp. 9844-9851
Notes: First up is the subject a paper that came out in ES&T a few years ago, where I investigated whether large scale wind power integration could have negative impacts on river ecosystems by further disrupting natural flow regime.

## Slide 35
NATURAL FLOW REGIME: the natural timing, magnitude frequency, rate-of-change and duration of streamflows
Depend on natural flows for: biological triggers; lifecycle processes; access to floodplain; protection against invasives
DAM IMPACTS
(flood control, water supply)
(autocorrelation)
Frequency
Timing
Rate-of-change
Magnitude
Duration
Notes: Again, this is a potential issue because flow regime is a really important factor determining the success of native species in rivers. And dams already significantly disrupt this balance. On monthly time steps, hydroelectric dams stamp out hydrologic extremes.

## Slide 36
Chart: River Discharge (1000 ft3/s)
0 24 48 72 96 120 144 168
Hour
OPERATIONAL FLEXIBILITY OF DAMS LEADS TO USE AS A ‘PEAKING’ RESOURCE
Notes: But on hourly time steps, hydroelectric dams impose a very predictable, but extreme flow pattern, which can have a range of ecological consequences for downstream areas. Now, the reason dams do this is to capture the highest possible value for the electricity they sell. Dams all over the country operate as peaking resources, meaning they only sell electricity when demand or the price of electricity is highest.

## Slide 37
Rapid changes in downstream water temperature, velocity, bed shear stress
River bottom can experience drying and wetting on a daily basis  stranding of fish and invertebrates
Ecological impacts of hydropower “peaking”
Sources: Zimmerman et al., 2010; Bevelhimer et al., 2014
Notes: But this behavior can be highly damaging, in particular it can cause stranding of fish and invertebrates because of rapid wetting and drying of the river bottom.

## Slide 38
Wind power integration & electricity markets
More wind  lower prices
Forecast errors increase demand for “reserves” (back-up)
High Wind
Quantity (MWh)
Price ($/MWh)
High Wind
Forecast
Errors
Hours
MWh
Wind Power Production (Forecast, Actual)
Notes: I was interested in quantifying the potential for increased penetration of wind power in electricity markets to exacerbate the impacts of dams on river ecosystems. This could happen if the presence of wind energy alters electricity prices in a way that incentivizes dam operators to follow more volatile reservoir release patterns. So, it’s important to consider how wind might actually change electricity prices. The prevailing hypothesis was that whenever wind is plentiful, it would suppress prices by lowering net demand for electricity. And second, I thought unexpected shortfalls in wind production would increase demand for ‘back-up’ for wind production that hydroelectric dams, because of their operational flexibility, are uniquely positioned to provide.

## Slide 39
Streamflow increase during low wind/shortfalls periods
Streamflow decrease during high wind/surplus hours
 Increased volatility
Will hourly streamflow patterns reflect wind dynamics in the future?
Cumulative sum of hour-to-hour fluctuations
Total Streamflow
RBF Index
=
High RBF
Low RBF
Source: Baker et al., 2004
Richards-Baker Flashiness Index
Notes: So the hypothesis was that we would see streamflow dynamics being driven directly by the availability of wind, where streamflows would increase during low wind/shortfall periods, and decrease during high wind/surplus hours, with that combining to increase the volatility of streamflows. We measured streamflow volatility using the Richards-Baker Flashiness Index, which quantifies within-day fluctuations relative to total streamflow.

## Slide 40
PJM
(Dominion Zone)
Roanoke River Basin, NC & VA
Notes: As a case study we looked at the operations of Roanoke Rapids Dam, which is the furthest downstream dam in the Roanoke River basin, which spans both North Carolina and Virginia. This dam is of interest for two reasons. First, downstream of the dam are significant conservation resources that are managed by the Nature Conservancy. And second, these dams sell electricity into a wholesale electricity market called PJM, which covers most of the Mid-Atlantic.

## Slide 41
0%, 5%, 15% and 25% average wind penetration
POWER SYSTEM MODEL
Chart: 
| Coal | Oil | Nuclear | Biomass | Natural Gas | Hydropower
 | 0.34622 | 0.015625 | 0.15586 | 0.019744 | 0.37628 | 0.086269
23,000 MW (Virginia)
Hydro, 9%
Baseline (no wind)
HYDROLOGIC
MODEL
HYDROPOWER
OPTIMIZATION
Electricity Prices
3 Wind Scenarios
Price changes incentivize dams to provide more wind “back-up”
Systems with high-wind capacity experience “flashier” streamflows
Marginal increase << original impacts of the dam
Streamflow
Notes: To answer this question, I built a power system model for the Dominion zone of PJM, and subjected it to three different levels of installed wind power capacity, simulated corresponding wholesale electricity prices, optimized reservoir releases for a profit maximizing hydroelectric dam, and looked at environmental flow patterns under baseline and wind conditions. What we found is that in general, days with really high wind penetration do result in price shifts that would incentivize dam owners to essentially provide back up for wind producers, and as a result systems with very high wind power capacity experience less natural flows; but, I should stress, that the marginal impacts associated with adding wind capacity are much smaller than the impacts of building the dam in the first place. So those are somewhat negative results, but this study is a perfect example of a class of problem I’m interested in, where shifts in technology can alter markets and the behavior of infrastructure systems and leave a signature on ecosystems.

## Slide 42
COULD FRACKING ALLEVIATE PRESSURE ON NATURAL FLOW REGIME IN RIVERS?
Kern, J.D., Characklis, G.W. (2016). “Low Natural Gas Prices and the Financial Cost of Ramp Rate Restrictions at Hydroelectric dams.” Energy Economics, Vol. 61, pp. 340-350
Notes: Another example of that, is the potential for fracking, and in particular, low natural gas prices, to make it cheaper to implement environmental flow provisions at dams.

## Slide 43
Chart: River Discharge (1000 ft3/s)
Chart: Hour
Environmental Restrictions
0 24 48 72 96 120 144 168
Hour
OPERATIONAL FLEXIBILITY OF DAMS LEADS TO USE AS A ‘PEAKING’ RESOURCE
Notes: Because of wider recognition of the negative impacts hydropower peaking on river ecosystems, in the last several decades there has been a legal push to restrict the ability of some dams to operate this way, either through federal relicensing or litigation. As you can imagine, there’s been a lot of resistance on the part of power companies.

## Slide 44
Chart: Hour
0 24 48 72 96 120 144 168
Off-peak hours
Peak hours
Chart: Quantity (GWh)
| 208 | 386 | 486 | 2123 | 2222.4 | 2661.7000000000003 | 3102.2000000000003 | 3586.0000000000005 | 4843 | 8323.4 | 10241.799999999999 | 10640.8 | 12525.9 | 13006.3 | 13336.3 | 15280.199999999999 | 16742.899999999998 | 18556.399999999998 | 19065.499999999996 | 19196.699999999997 | 19562.499999999996 | 19666.699999999997
 | 0 | 0 | 0 | 8.11 | 14.5772 | 16.6042 | 17.5116 | 18.0023 | 18.88 | 18.8992 | 19.7572 | 29.54 | 30.9252 | 31.7672 | 34.77 | 51.96 | 68.4781 | 68.6012 | 75.13 | 229.7367 | 302.1641 | 308.7309
0 5 10 15 20 25
Peak
Demand
Off-Peak
Demand
Spread =
$65/MWh
Chart: Quantity (GWh)
| 208 | 386 | 486 | 2123 | 2222.4 | 2661.7000000000003 | 3102.2000000000003 | 3586.0000000000005 | 4843 | 8323.4 | 10241.799999999999 | 10640.8 | 12525.9 | 13006.3 | 13336.3 | 15280.199999999999 | 16742.899999999998 | 18556.399999999998 | 19065.499999999996 | 19196.699999999997 | 19562.499999999996 | 19666.699999999997
 | 0 | 0 | 0 | 8.11 | 14.5772 | 16.6042 | 17.5116 | 18.0023 | 18.88 | 18.8992 | 19.7572 | 29.54 | 30.9252 | 31.7672 | 34.77 | 51.96 | 68.4781 | 68.6012 | 75.13 | 229.7367 | 302.1641 | 308.7309
0 5 10 15 20 25
Spread =
$30/MWh
Chart: Quantity (GWh)
| 208 | 386 | 486 | 2123 | 2222.4 | 2661.7000000000003 | 3102.2000000000003 | 3586.0000000000005 | 4843 | 8323.4 | 10241.799999999999 | 10640.8 | 12525.9 | 13006.3 | 13336.3 | 15280.199999999999 | 16742.899999999998 | 18556.399999999998 | 19065.499999999996 | 19196.699999999997 | 19562.499999999996 | 19666.699999999997
 | 0 | 0 | 0 | 8.11 | 14.5772 | 16.6042 | 17.5116 | 18.0023 | 18.88 | 18.8992 | 19.7572 | 29.54 | 30.9252 | 31.7672 | 34.77 | 51.96 | 68.4781 | 68.6012 | 75.13 | 229.7367 | 302.1641 | 308.7309
0 5 10 15 20 25
Coal
Natural
Gas
Low gas prices
Notes: This type of operational restriction essentially forces dam owners to sell equal amounts of electricity during low value, “off peak” hours and high value “peak” hours. The financial penalty associated with this is proportional to the difference (or spread) between the peak and off peak price. Which, at least historically, have corresponded to the difference between generating electricity from a coal plant in off peak hours and generating electricity from a natural gas plant during peak hours. So what happens if natural gas prices decline? The portion of the supply curve associated with natural gas plants decreases. And now the peak-off peak price spread is much narrower.

## Slide 45
Chart: Month/Year
Chart: 
Gas Price ($/MMBtu)
Can low natural gas prices be exploited to impose more natural flow regimes at dams?
Hurricane
Katrina
Financial
Crisis
Fracking
Roanoke River Dam, NC
Notes: So the question here is given the fact that natural gas prices have declined and stayed persistently low in the last decade, can this be exploited to impose more natural flow regimes at dams at a lower cost. My modeling results confirmed this. In fact, the cost has become so low, it could raise the possibility that at some dams conservation trusts may now be in a position to purchase peaking restrictions directly from dam owners, as an alternative to litigation. There is a reasonable amount of precedent for this idea, but in this case there’s a major problem.

## Slide 46
18.5
15.5
12.5
9.5
6.5
3.5
0.5
10 40 70 100 130 160
Peak/Off-Peak Price Spread ($/MWh)
1
0.8
0.6
0.4
0.2
Inflows (kcfs)
Cost of Restrictions ($M)
VERY WET PERIOD: dams must release maximum discharge 24/7 (no peaking)
VERY DRY PERIOD: dams must release minimum discharge 24/7 (no peaking)
Spread Natural Gas Price
Chart: 
Gas Price ($/MMBtu)
Hurricane
Katrina
Financial
Crisis
Fracking
Notes: It turns out the cost of imposing peaking restrictions at dams is not only a function of gas prices and peak/off-peak price spread, it’s also highly sensitive to hydrologic variability. During very wet periods and very dry periods, the cost of ramping restrictions for a dam owner is essentially 0, because it would have a very limited ability to use the dam as a peaking resource. The cost of restrictions is highest during moderate flow periods.

## Slide 47
Chart: Monthly Cost of Restrictions ($M)
| 0 - 0.1 | 0.1 - 0.2 | 0.2 - 0.3 | 0.3 - 0.4 | 0.4 - 0.5 | 0.5 - 0.6 | 0.6 - 0.7 | 0.7 - 0.8 | 0.8 - 0.9 | 0.9 - 1 | 1 - 1.1 | 1.1 - 1.2 | 1.2 - 1.3 | 1.3 - 1.4 | 1.4 - 1.5 | 1.5 - 1.6 | 1.6 - 1.7 | 1.7 - 1.8 | 1.8 - 1.9 | 1.9 - 2 | 2 - 2.1 | 2.1 - 2.2 | 2.2 - 2.3 | 2.3 - 2.4 | 2.4 - 2.5 | 2.5+
 | 0.007 | 0.04 | 0.098 | 0.151 | 0.159 | 0.145 | 0.112 | 0.063 | 0.037 | 0.036 | 0.027 | 0.02 | 0.017 | 0.013 | 0.01 | 0.007 | 0.01 | 0.003 | 0.005 | 0.008 | 0.001 | 0.003 | 0.004 | 0.004 | 0.002 | 0.003
mean
> 3x mean
Notes: there is a high degree of uncertainty about the cost of restrictions. What this means is that if a conservation trust and dam owner agreed ex ante to impose restrictions, with the trust responsible for making the dam owner whole after the fact, the trust could be putting itself at considerable risk.

## Slide 48
Dam
Owner
Third Party Insurer
Conservation Trust
Natural
Flows
Cost of Restrictions
Notes: The only way for this to conceivably work is if the conservation trust engaged a third party financial institution, a bank or insurer, to absorb that risk for a fee. So as part of this work, I developed a hypothetical contract to facilitate agreements like this.

## Slide 49
Dam
Owner
Conservation Trust
Insurer Pays Conservation Trust
Natural
Flows
Cost of Restrictions
Notes: And when the cost of restrictions is higher than the expected value, the insurer pays the conservation trust the difference. This essentially guarantees that the trust would always pay the expected value of the cost of restrictions, plus a loading premium to incentivize the insurer to take that risk.

## Slide 50
Dam
Owner
Conservation Trust
Conservation Trust
Pays Insurer
Natural
Flows
Cost of Restrictions
Notes: The way it works is that whenever the cost of restrictions turns out to be lower than the expected cost, the conservation trust actually pays the insurer the difference.

## Slide 51
Dam
Owner
Conservation Trust
Expected Value
Cost
Third Party Insurer
Natural
Flows
Cost of Restrictions
Notes: And when the cost of restrictions is higher than the expected value, the insurer pays the conservation trust the difference. This essentially guarantees that the trust would always pay the expected value of the cost of restrictions, plus a loading premium to incentivize the insurer to take that risk.

## Slide 52
Kern, J.D., Characklis, G. (2017). “Evaluating the Financial Vulnerability of a Major Electric Utility in the Southeastern U.S. to Drought under Climate Uncertainty and an Evolving Generation Mix.” Environmental Science and Technology. Vol. 55 (15), pp. 8815-8823
WILL DROUGHT POSE a EXISTENTIAL RISK for SOUTHEASTERN ELECTRIC POWER UTILITIES in the FUTURE?
Notes: Next I’d like to talk about a study that investigated drought as a future source of risk for power utilities in the southeast.

## Slide 53
KW = power capacity of plant
ηtotal = fraction of total input heat from fuel that is converted to electricity
= heat rate
= the portion of the waste heat that is not discharged by cooling water
q = flow rate of power plant water withdrawal
ρw = density of water
Cp = heat capacity of water
Tin = intake water temperature
Tout = effluent water temperature
HEAT TRANSFER DEMAND
Drought Impacts on Power Systems
FLOW
IN/OUT TEMPS
COOLING WATER
Hydropower (1:1 loss with streamflow)
Thermal plants (nuclear, coal)
Notes: The most obvious way drought impacts power systems is by reducing hydropower production. But it can also impact thermal power plants, especially older coal and nuclear plants that employ open loop cooling systems and are located on rivers. Thermal power plants require a certain amount of heat to be transferred from the steam cycle. This is done via cooling water, which is brought in from a river or lake, heated up and then discharged back into the water body.

## Slide 54
HEAT TRANSFER DEMAND
FLOW
+
-
Drought Impacts on Power Systems
Hydropower (1:1 loss with streamflow)
Thermal plants (nuclear, coal)
Influent temperatures () spike
due to low flows, high temps
-
Drought
Deviation from species’ thermal preferences, upper tolerance; lower dissolved oxygen  species distribution, growth rates
THERMAL POLLUTION and RIVER ECOSYSTEMS
REGULATORY CONSTRAINTS
Notes: But, in many cases there are regulatory limits on maximum effluent temperature from power plants, as well as the differential between input and output temperatures. These are in place to protect freshwater ecosystems from thermal pollution which can push species beyond their thermal preferences or tolerances, as well as lower dissolved oxygen availability. Now, during a drought ….

## Slide 55
Chart: Quantity (GWh)
| 208 | 386 | 486 | 2123 | 2222.4 | 2661.7000000000003 | 3102.2000000000003 | 3586.0000000000005 | 4843 | 8323.4 | 10241.799999999999 | 10640.8 | 12525.9 | 13006.3 | 13336.3 | 15280.199999999999 | 16742.899999999998 | 18556.399999999998 | 19065.499999999996 | 19196.699999999997 | 19562.499999999996 | 19666.699999999997
 | 0 | 0 | 0 | 8.11 | 14.5772 | 16.6042 | 17.5116 | 18.0023 | 18.88 | 18.8992 | 19.7572 | 29.54 | 30.9252 | 31.7672 | 34.77 | 51.96 | 68.4781 | 68.6012 | 75.13 | 229.7367 | 302.1641 | 308.7309
0 5 10 15 20 25
Normal Price
EXACERBATED BY CLIMATE CHANGE
2000-2001 California Electricity Crisis
Drought Price
Hydropower (global)
10
5
0
-5
-10
-15
Change in usable capacity (%)
1970 2000 2030 2060 2090
Van Vliet et al., 2016
1970 2000 2030 2060 2090
Thermal Capacity (global)
Control
RCP 2.6
RCP 8.5
0
-10
-20
-30
10
Change in usable capacity (%)
Notes: Losing a combination of hydropower and baseload nuclear or coal has the effect of shifting the system supply curve to the left, potentially causing a spike in electricity prices, and historically this has caused problems in power systems. In recent years a number of high profile papers have come out warning against the long term impacts of climate change on both hydropower generation and thermal generation.

## Slide 56
CRITICAL GAPS IN KNOWLEDGE:
Financial Risk
  Does enforcement of thermal pollution regulations during drought threaten returns for utility investors?
      Important decision criteria
Shifting generation mix
Most vulnerable thermal plants to cooling water issues (older coal plants) are being retired
    Replaced by natural gas and renewables
Drought Impacts on Power Systems
Notes: But there were a couple critical gaps in knowledge. First, there had been no attempt to understand whether these losses poses risks for investors of utilities (both shareholders and lenders), which is an important criteria for decision makers at utilities. Nor had there been any attempt to understand how rapid changes in the underlying generation mix could alter utilities exposure to drought. This is important, because many of the plants that are most vulnerable to cooling water issues (older coal plants) are being retired.

## Slide 57
Chart: Annual Hydro Production (GWh)
Chart: 
Lower “low flows” (10th percentile)
Higher thermal capacity losses
Higher summer electricity demand
Solar
Storage
Thermal
Losses
Load
Reservoir Network Model
Gas Prices
Energy Sales Variable Costs
Fixed Costs
Prices, Revenues
and Risk
Corporate Finance
UC/ED
Temperature
Streamflow
Hydropower
Portfolios
Baseline
Coal-to-gas
Solar PV
1970-2010
2040s (B1)
Climate
Baseline (coal heavy) (2010)
Coal-to-gas switch (2017)
Solar: 1000-4000 MW
DEC System:
18,000 MW
$2.5/MMBtu (2016)
$5/MMBtu (historical avg.)
$7.5/MMBtu
Stochastic streamflow and temperature
Cool & Wet
Hot & Dry
Notes: So I built a comprehensive model of the Duke Energy Carolina’s system in NC and then subjected this model to different climate scenarios, different generation portfolios and natural gas prices. And I took this matrix of scenarios and subjected each one to 1000 years of stochastic weather data.

## Slide 58
10
8
6
4
2
0
Density (e-9)
1970-2010
1970-2010
9.0%
9.2%
9.4%
9.6%
9.8%
10%
Return on Equity
3
2
1
0
Density (100s)
12
Increases 1-year system costs up to $300 million
Maximum 1-year profit loss of $180 million
No impact to debt service; modest impact to shareholders (target is $2 billion for 10% return on equity)
Deviation Above Expected Cost
0(μ) + $100M + $200M + $300M
Notes: Our results suggest that in the worst-case scenario, Duke’s 1-year costs could increase by about $300 million dollars, and their potential profit shortfall is about $180 million dollars. Now that sounds like a awfully big number, but their target operating income is on the order $2 billion. So, this means Duke’s never going to go bankrupt from drought. And it only moderately reduces returns for shareholders. That’s great, at least they thought so when we told them, but one cause for concern here is that a lack of financial risk doesn’t mean there’s no risk to system reliability. I think the danger is that a lack of serious financial consequences may lure some utilities to sleep with respect to the threat drought can pose to their systems physical integrity.

## Slide 59
Current/Future Projects
Notes: I also want to mention some current and future funded projects that I’m involved in, the first is one that focuses on the design of sustainable algal biofuel production facilities.

## Slide 60
DESIGNING FUTURE SUSTAINABLE ALGAL BIOFUEL PRODUCTION FACILITIES
U.S. Dept. of Energy Productivity Enhanced Algae and Took-Kits (PEAK)

## Slide 61
Algal Biofuel Pathways
Cultivation
Harvesting
Conversion
Water
Nutrients
Energy
Energy
Energy
Closed Loop Systems & Industrial Ecology
Global Warming Potential (% of diesel)
Minimum Fuel
Price ($/gge)
High Value Products
(chemicals, nutraceuticals, animal feed, etc.)
Municipal Wastewater
Notes: Algae really is a really interesting resource: compared to crop based biofuels, it’s is better able to produce a diverse set of products, recovering valuable inputs, and integrating with other industrial processes. The cost of algal biofuels is not currently competitive with conventional fuels, but it is coming down. And the field is approaching the point where it needs to start to think more broadly about how to make these systems work, and in particular, how they would interact with other human systems and the natural environment.

## Slide 62
Multi-objective Optimal Plant Siting
WWTP Compliance
Association
Upstream
Downstream
TMDL
Algae Producer:
Maximize Profits
WWTPs:
Minimize Costs
Fertilizer replacement
N, P removal
WWTP Plant
Notes: For example, one project I have that is still somewhat ongoing looks at tradeoffs that arise when siting algae biofuel facilities within impaired watersheds. Let’s say you identify an ideal region for cultivating algae for biofuel production and then you want to co-locate algae production with an existing wastewater treatment plant. In theory, the algae would provide monetizeable tertiary treatment in the form of Nitrogen and Phosphorus removal, and the wastewater itself would help offset the cost of fertilizer. But because algae producers want to maximize profits and treatment plants would want to collectively minimize costs of adhering to a downstream TMDL, there’s a good chance that the best place location for making a profit on algae is not be the best location for minimizing the cost of meeting the TMDL, and that means there is no single optimal way to do it, instead there are tradeoffs between these two objectives.

## Slide 63
Multi-objective Optimal Plant Siting
WWTP Compliance
Association
Upstream
Downstream
TMDL
WWTP Plant
Notes: For example, one project I have that is still somewhat ongoing looks at tradeoffs that arise when siting algae biofuel facilities within impaired watersheds. Let’s say you identify an ideal region for cultivating algae for biofuel production and then you want to co-locate algae production with an existing wastewater treatment plant. In theory, the algae would provide monetizeable tertiary treatment in the form of Nitrogen and Phosphorus removal, and the wastewater itself would help offset the cost of fertilizer. But because algae producers want to maximize profits and treatment plants would want to collectively minimize costs of adhering to a downstream TMDL, there’s a good chance that the best place location for making a profit on algae is not be the best location for minimizing the cost of meeting the TMDL, and that means there is no single optimal way to do it, instead there are tradeoffs between these two objectives.

## Slide 64
Multi-objective Optimal Plant Siting
Upstream
Downstream
Effluent discharge & N concentration
  N removal per unit algae
  Total supply of N
LULC and topography
  Maximum algae production capacity
Land costs ($/acre)
  Algae capex
N transfer coefficients
  Contribution to TMDL
Site Characteristics Drive Tradeoffs
10%
90%
TMDL
WWTP Compliance
Association
WWTP Plant
Algae producers:
High effluent concentration
WWTPs
High N transfer coefficient
X
X
Notes: These tradeoffs are likely to be driven by differences in site characteristics like effluent volume and concentration, land type and topography which control the amount land available for algae cultivation at each site, and also the natural attenuation of N in the waterway, which makes N removal more valuable closer to the estuary. For example, WWTPs plants may prefer sites with a higher N transfer coefficients, while algae producers may prefer sites with higher N effluent concentration, and it’s possible neither would get their wish if local LULC and topography don’t support large scale algae production.

## Slide 65
Multi-objective Optimal Plant Siting
Upstream
Downstream
TMDL
$$$
$$$
$$$
$
$$
$
WWTP Compliance
Association
Effluent discharge & N concentration
  N removal per unit algae
  Total supply of N
LULC and topography
  Maximum algae production capacity
Land costs ($/acre)
  Algae capex
N transfer coefficients
  Contribution to TMDL
Site Characteristics Drive Tradeoffs
WWTP Plant
Nutrient Trading
Market
Notes: And all of this can also be complicated by the presence of nutrient trading markets, which allow treatment plants with higher mitigation costs to pay other plants to remove nitrogen instead. We were specifically interested in the role of nutrient trading markets in increasing siting flexibility for algae producers, since they would allow nitrogen removed using algae anywhere in the basin to be fully monetized.

## Slide 66
Slope
Coeff.
= 1.0
= .7
= .5
= .1
75%
0%
Land
Type
Urban
Woody
Agr.
Wetland
Land
Cost
($/ha)
6150
2150
Major WWTP
TMDL
Notes: We chose as a case study, the Neuse River basin, and specifically focused on a group of major WWTPs that form a compliance association, which means that they can, if desired, work together to collectively meet the downstream TMDL for nitrogen if that’s cheaper than each plant individually adhering to it’s permitted discharge.

## Slide 67
Multi-objective Optimal Plant Siting
Decision Variables:
How much algae to grow at each WWTP?
Algae Profits ($)
WWTP Costs ($)
Ideal Point
Upstream
Downstream
NSGA-II (genetic algorithm)
Neuse River Compliance Association (NRCA)
TMDL
Notes: And then I used a multi-objective evolutionary algorithm to essentially map individual scenarios where algae is sited in different places, to a 2-dimensional score over here, where the ideal point is in the bottom right corner.

## Slide 68
Chart: Effluent Conc. (mg/L)
 | 3.24 | 4.21 | 3.72 | 3.49 | 3.71 | 3.69 | 5.74 | 1.74 | 3.02 | 3.97 | 3.98 | 3.01 | 3.91 | 3.87 | 3.7 | 3.75 | 5.51 | 5.51 | 3.51
Chart: Max Land (ha)
 | 0 | 47.8537 | 98.9906 | 42.5465 | 120.3601 | 4.2818 | 74.8123 | 47.1323 | 27.1254 | 86.0563 | 63.8408 | 50.5656 | 0 | 56.7175 | 6.0833 | 57.1406 | 35.9614 | 0 | 30.7406
Chart: Land Cost ($/ha)
 | 4444.4444 | 5333.3333 | 6148.1481 | 5407.4074 | 6148.1481 | 3851.8519 | 5259.2593 | 5259.2593 | 5259.2593 | 5333.3333 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 2148.1481 | 2148.1481 | 2666.6667
Chart: Transfer Coeff.
 | 1 | 0.7 | 0.7 | 0.7 | 0.7 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.1 | 0.1 | 0.1
Sensitivity Analysis (80 runs)
Notes: We also performed a sensitivity analysis, to test the robustness of the tradeoffs identifed, where we randomly resampled site parameters without replacement, and we did this 20 times while holding everything else constant for 4 key parameters.

## Slide 69
Chart: Effluent Conc. (mg/L)
 | 3.24 | 4.21 | 3.72 | 3.49 | 3.71 | 3.69 | 5.74 | 1.74 | 3.02 | 3.97 | 3.98 | 3.01 | 3.91 | 3.87 | 3.7 | 3.75 | 5.51 | 5.51 | 3.51
Chart: Land Cost ($/ha)
 | 4444.4444 | 5333.3333 | 6148.1481 | 5407.4074 | 6148.1481 | 3851.8519 | 5259.2593 | 5259.2593 | 5259.2593 | 5333.3333 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 2148.1481 | 2148.1481 | 2666.6667
Chart: Transfer Coeff.
 | 1 | 0.7 | 0.7 | 0.7 | 0.7 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.1 | 0.1 | 0.1
Chart: Max Land (ha)
 | 47.1323 | 98.9906 | 74.8123 | 57.1406 | 63.8408 | 6.0833 | 120.3601 | 50.5656 | 56.7175 | 4.2818 | 47.8537 | 27.1254 | 42.5465 | 0 | 35.9614 | 0 | 0 | 86.0563
Sensitivity Analysis (80 runs)

## Slide 70
Chart: Effluent Conc. (mg/L)
 | 3.24 | 4.21 | 3.72 | 3.49 | 3.71 | 3.69 | 5.74 | 1.74 | 3.02 | 3.97 | 3.98 | 3.01 | 3.91 | 3.87 | 3.7 | 3.75 | 5.51 | 5.51 | 3.51
Chart: Land Cost ($/ha)
 | 4444.4444 | 5333.3333 | 6148.1481 | 5407.4074 | 6148.1481 | 3851.8519 | 5259.2593 | 5259.2593 | 5259.2593 | 5333.3333 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 2148.1481 | 2148.1481 | 2666.6667
Chart: Transfer Coeff.
 | 1 | 0.7 | 0.7 | 0.7 | 0.7 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.1 | 0.1 | 0.1
Chart: Max Land (ha)
 | 47.1323 | 57.1406 | 0 | 42.5465 | 63.8408 | 120.3601 | 98.9906 | 35.9614 | 0 | 6.0833 | 74.8123 | 86.0563 | 47.8537 | 50.5656 | 56.7175 | 0 | 4.2818 | 27.1254
Sensitivity Analysis (80 runs)

## Slide 71
Chart: Effluent Conc. (mg/L)
 | 3.24 | 4.21 | 3.72 | 3.49 | 3.71 | 3.69 | 5.74 | 1.74 | 3.02 | 3.97 | 3.98 | 3.01 | 3.91 | 3.87 | 3.7 | 3.75 | 5.51 | 5.51 | 3.51
Chart: Land Cost ($/ha)
 | 4444.4444 | 5333.3333 | 6148.1481 | 5407.4074 | 6148.1481 | 3851.8519 | 5259.2593 | 5259.2593 | 5259.2593 | 5333.3333 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 3851.8519 | 2148.1481 | 2148.1481 | 2666.6667
Chart: Transfer Coeff.
 | 1 | 0.7 | 0.7 | 0.7 | 0.7 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.1 | 0.1 | 0.1
Chart: Max Land (ha)
 | 56.7175 | 57.1406 | 98.9906 | 74.8123 | 35.9614 | 4.2818 | 6.0833 | 50.5656 | 47.1323 | 27.1254 | 0 | 86.0563 | 63.8408 | 0 | 42.5465 | 120.3601 | 47.8537 | 0
20
20
20
20
Sensitivity Analysis (80 runs)

## Slide 72
Market
Ideal
Point
Ideal
Point
Algae Profits ($100,000s)
Original
Tradeoff
Frontier
Sensitivity
Analysis
Ideal
Point
Ideal
Point
Nutrient trading markets add important flexibility
Protect against uncertainty in watershed parameters.
NRCA Cost ($100,000s)
NRCA Cost ($100,000s)
No Market
Algae Profits ($100,000s)
Notes: We did find some interesting siting tradeoffs in the Neuse, but I actually thought the most important result was related to the role of nutrient trading markets in adding siting flexibility. For instance, when we randomly reassigned parameters as part of the sensitivity analysis, without a market in place we saw serious potential for worse outcomes in both objectives, which are shown in the red triangles here. That suggests that in watersheds that don’t look like the Neuse, the value of co-locating algae biofuel production with WWTPs could be a lot different. But with the market in place, there’s a lot more flexibility in choosing the best sites, and that flexibility ends up protecting both objectives from experiencing worse values. What this suggests is that the presence of nutrient trading markets, if they’re used, is key to finding sites for locating algae production that work for both parties.

## Slide 73
WATER SUPPLY VULNERABILITIES and ADAPTATION OPPORTUNITIES in CALIFORNIA’S COUPLED AGRICULTURAL and ENERGY SECTORS
NSF INNOVATIONS AT THE NEXUS OF FOOD, ENERGY AND WATER SYSTEMS (INFEWS) – TRACK 2
Notes: I’m also the co-PI of a project funded through the NSF INFEWS program, it’s a 4 year project which is at the halfway point. This one is focused on identifying strategies at a large scale for balancing agricultural production in California with sustainable patterns of water and electricity consumption, under climatic, regulatory and market uncertainty.

## Slide 74
The Central Valley – most productive agricultural area in the U.S.
  Major statewide water user
Central Valley Water Supply (MAF)
Groundwater
Surface
Water
1979
1989
2009
1999
15
10
5
Notes: A major focus of the project is on how drought ties together groundwater pumping in the central valley and the electric power sector. The central valley…

## Slide 75
The Central Valley – most productive agricultural area in the U.S.
  Major statewide water user
Delta Smelt – Spring Adult Index
Notes: Increasingly, that operational paradigm is being threatened by a combination of forces. First, drastic declines in the endangered delta smelt, which is an indicator species for the larger Sacramento-San Joaquin basin, has reduced the amount of snowmelt that is diverted out of the basin and sent down to the Central Valley via aqueduct to be used as irrigation. As you can imagine, this has raised the ire of the agriculture industry, which has had to increase its dependency on more expensive groundwater.

## Slide 76
The Central Valley – most productive agricultural area in the U.S.
  Major statewide water user
  Shift toward permanent crops and “hardened” demand
Cumulative Groundwater Loss (km3)
Wet
Wet
Dry
Dry
0
-40
-80
-120
1965 1975 1985 1995 2005 2015
Notes: At the same time, the region has been marked by a shift away from row crops towards permanent fruit and nut trees which has hardened demand for water. All of these factors, in combination with recent droughts, has driven ground water level to historical lows, and the state is actually permanently losing groundwater storage capacity because of land subsidence.

## Slide 77
Chart: 
 | 8 | 3 | 12 | 12 | 65
ASSOCIATED GRID IMPACTS
Energy demand for water delivery (TWh)
2
1
0
Oct. Dec. Feb. Apr. June Aug.
Groundwater
State Water Project
Central Valley Proj.
Colorado River Aqu.
80
40
0
Jan ’06 Jan ’08 Jan ‘10 Jan ‘12 Jan ‘14
Natural Gas
Hydropower
% of Total Electricity Generation
DROUGHT IMPACTS
1:1 replacement of hydro with natural gas
Higher groundwater pumping energy
California
Mix
(2015)
Other
Notes: At the same time, drought in California hits the power sector pretty hard. Lost hydropower production is replaced 1 for 1 with natural gas generation, which shifts the supply curve up and over to the left, increasing prices. What this means, is that wholesale prices increase precisely when irrigators are pumping the most groundwater, which already occurs during high demand summer months, and all this is made worse by the fact that low groundwater levels mean pumping is a more energy intensive process.

## Slide 78
Irrigation districts
Growers
Environment & Conservation
Electric utilities
Retail electricity customers
Risks for Stakeholders
Interest of Key Policy Makers
California Department of Water Resources
Public Policy Institute of California
California Energy Commission
California Independent System Operator
KERN
WATER BANK
AUTHORITY
Notes: This situation poses a number of risks, for growers, irrigation districts, and electric utilities. And we’ve also piqued the interest of key policy makers in the state. Right now all these folks are working directly with us.

## Slide 79
Systems Dynamics Simulation Model
Notes: The main product will be an open source tool that combines a comprehensive systems dynamics model and many objective evolutionary algorithms to evaluate key vulnerabilities and tradeoffs, and design robust portfolios of management solutions. I know this spaghetti diagram is a little hard to unpack.

## Slide 80
CAPOW! – Multi-zone stochastic water-power simulation model for California and the larger West Coast wholesale market

## Slide 81
CAPOW! – Multi-zone stochastic water-power simulation model for California and the larger West Coast wholesale market
March 2015 - Drought
March 2017 - Flood

## Slide 82
LEVERAGING NATURAL RESOURCE CONCENTRATION and CONVEYANCE in the ENERGY WATER FOOD NEXUS to INCREASE SECURITY and RESILIENCE
NSF INNOVATIONS AT THE NEXUS OF FOOD, ENERGY AND WATER SYSTEMS (INFEWS) – TRACK 1
Notes: I am also involved in another successful INFEWS proposal that just started, which is focused on a similar mix of issues but is oriented more towards the Pacific Northwest.

## Slide 83
Federally owned dams with multi-objective tradeoffs
Water supply, environmental flows, flood control, hydropower
Major challenges: climate change (streamflow dynamics), renewables and population growth
Lookout Point Dam, OR
Willamette River Basin
< 2%
Notes: Specifically the Willamette River Basin, which is a tributary of the Columbia. In the Willamette there is a network of 13 federal dams that have multi-purpose obligations to provide water supply, flood control, and hydropower, as well as support riparian ecosystems. The goal of the project is to develop strategies for balancing these objectives under future stress, with the primary expected impacts coming from climate change and population growth. My group will be helping to address these issues by using a fully coupled representation of surface water and power system dynamics for the entire west cost.

## Slide 84
Thank you very much for listening!
EMAIL
jdkern@live.unc.edu
WEB
http://jdkern.web.unc.edu/
Notes: So with that, I’ll say thank you very much for listening, and I’m happy to take questions.